## Slide 1
COMPUTATIONAL DATA SCIENCE • PROJECT PRESENTATION
From Sensor Readings to Gait Insights
Exploratory Computational Analysis of Wearable Inertial Sensor Data
Grishma Makwana • 23BIT108 Prerita Shukla • 23BIT119

## Slide 2
The complete project pipeline
ROADMAP
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
02
01 Hardware
ESP32 + IMU sensor
02 Acquire
Walking trials
03 Organize
Timestamped CSV files
04 Validate
Quality and timing checks
05 Explore
Visualize six channels
06 Transform
Windows and features
07 Compare
Paired statistics
08 Investigate
PCA, clustering, ML
OUTPUT: quality reports • feature tables • participant-level comparisons • exploratory visualizations
The goal is a transparent workflow from physical measurement to interpretable evidence—not a clinical diagnosis.

## Slide 3
Motivation and potential applications
CONTEXT
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
03
Why study wearable gait signals?
• Raw accelerometer and gyroscope readings are difficult to interpret directly. • Computational methods can summarize movement patterns as numerical features. • Within-person left–right comparisons require careful analysis and uncertainty reporting.
Movement monitoring
Explore changes in movement signals over time.
Rehabilitation research
Potential support for studying movement consistency—not a validated clinical tool.
Wearable analytics
A foundation for future sensor-based analysis systems.
Scope boundary: this project explores a computational workflow; it does not diagnose gait disorders.

## Slide 4
Hardware design and sensor selection
ACQUISITION
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
04
Controller
ESP32 microcontroller
Motion sensor
GY-521 module with MPU6050 IMU
Communication
I²C
SDA GPIO 21
SCL GPIO 22
Configured ranges
Accelerometer ±2 g and Gyroscope ±250°/s
The IMU measures acceleration and angular velocity on three axes each, producing six motion-related channels.

## Slide 5
Data collection: from walking to raw readings
ACQUISITION
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
05
1. Mount
Shin below knee; inverted orientation, top facing ground.
2. Record
Barefoot walking on a flat surface; approximately 10 seconds per leg.
3. Capture
Serial Monitor output copied and saved as CSV using Python.
Sampling interval
20 ms nominal
Sampling frequency
50 Hz nominal
Readings per trial
~500 samples

## Slide 6
Dataset overview and data quality
DATA
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
06
24
CSV files
12
participants
~500
samples / recording
50 Hz
nominal rate
Timestamp
Time_ms — used to inspect timing and intervals.
Accelerometer
AccelX/Y/Z_g — acceleration in g.
Gyroscope
GyroX/Y/Z_dps — angular velocity in degrees/second.
Quality checks to report
• Missing / infinite values • Duplicate timestamps and irregular intervals • Constant channels, abrupt cutoffs and extreme values
• 498–500 rows per recording, 9.96–9.98 s, 50.0 Hz estimated from Time_ms
• No missing, duplicate or constant values; 5 recordings with dropped samples or a late start
• About 12% of samples sit at the ±2 g / ±250 °/s limits (probable range limit, not confirmed saturation)

## Slide 7
Computational workflow and signal exploration
EDA
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
07
Inspect patterns
Variation, spikes, plateaus and changes over time.
Check orientation
Gravity direction and sensor mounting affect channel values.
Flag uncertainty
An extreme value may reflect movement or measurement artefact.

## Slide 8
Signal processing and feature extraction
REPRESENTATION
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
08
Raw signals
Six channels + timestamps
→
Windowing
Fixed-length segments
→
Feature table
Numerical descriptors
Time-domain features
Mean • variance • min/max • peak-to-peak • RMS • energy
Magnitude features
Acceleration and gyroscope vector norms; magnitude variability
Frequency-domain features
Dominant frequency • spectral energy
Cross-channel features
Axis correlations and selected channel relationships
Verified settings: 2.0 s windows (100 samples) • 50% overlap • 215 windows from 24 recordings • 184 features per row (183 testable)

## Slide 9
Statistical analysis: comparing left and right
INFERENCE
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
09
Participant 1
Left
Feature
Right
Feature
→
Within-person difference
Participant 2
Left
Feature
Right
Feature
→
Within-person difference
Participant 3
Left
Feature
Right
Feature
→
Within-person difference
Participant 4
Left
Feature
Right
Feature
→
Within-person difference
Paired inference
Compare legs within each participant.
Uncertainty
Effect sizes and confidence intervals.
Multiplicity
Correct for testing many features.
Why participant-level pairing?
Windows and samples from one person are not independent participants.
N = 12 participant pairs (24 recordings)
183 features tested; 0 significant after BH / Holm correction

## Slide 10
Exploratory machine learning
UNSUPERVISED / MODELS
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
10
PCA
Summarize variation in feature space.
Clustering
Explore whether feature vectors group together.
Anomaly detection
Flag windows unusual under a chosen model.
Classification
Test left/right predictability cautiously.
Interpretation: exploratory structure or unusual windows do not by themselves establish biological categories or abnormal gait.

## Slide 11
Key findings, limitations and future work
TAKEAWAYS
WEARABLE IMU • EXPLORATORY COMPUTATIONAL ANALYSIS
11
What the data supports
• Signals show clear periodic gait-like structure, but about 12% of samples sit at the ±2 g / ±250 °/s limits.
• Paired analysis (12 participants, 183 features): no left/right difference established; none survive correction.
• Exploratory ML is inconclusive: classifier 0.63 (exact p = 0.075); outliers and clusters track participant and movement intensity.
Current limitations
• Small participant cohort and short trials • Axis mapping / orientation uncertainty • Possible saturation or firmware clamping • No validated clinical ground truth
Future Scope
Longer, repeated trials
Standardized mounting and better wearable apparatus.
Expand participant cohort
Need Variety of people (with minor or major injuries in legs) for better model training.

## Slide 12
CONCLUSION
From physical measurement to computational insight
A documented pipeline transforms wearable IMU recordings into quality checks, interpretable features, participant-level comparisons and exploratory machine-learning outputs.
Main contribution
A transparent and reproducible analysis workflow.
Scientific boundary
Current results are exploratory, not clinically validated.
Thank you